## Slide 1
Reproducing BBR: A Controlled Study of Bottleneck-Based Congestion Control
CS 552 — Computer Networks · Spring 2026 · Rutgers University
Mihir Kulkarni · Chaitanya Ranaware · Piyoosha Gadi · Prof. Minsung Kim
We empirically reproduced Google's BBR algorithm against CUBIC and RENO on a controlled Linux testbed. Three experiments, one finding: BBR trades a small throughput gap for much lower latency.

## Slide 2
The Problem: Loss-Based Congestion Control
For over 30 years, TCP congestion control has relied on a single signal: packet loss. Algorithms like RENO and CUBIC accelerate until packets drop, then back off. This worked when router buffers were small — but modern hardware ships with megabytes of buffering, and the old model breaks down.
Buffer Bloat
A loss-based sender fills the router buffer before receiving a loss signal. Throughput looks fine, but queuing delay balloons — latency spikes even while the link is fully utilized.
The Core Question
Can we perform congestion control without using loss as the signal? BBR's answer: model the physical properties of the path itself — bandwidth and propagation delay — and operate at the optimal point.

## Slide 3
BBR's Idea: Model the Path
BBR estimates two physical quantities and uses their product — the Bandwidth-Delay Product (BDP) — as the target for in-flight data. This keeps the link full without queuing packets.
BtlBw — Bottleneck Bandwidth
The maximum delivery rate observed on the path. BBR paces its sending rate at this value to fully utilize the link.
RTprop — Propagation Delay
The minimum RTT observed, representing the path's physical propagation delay with no queuing. BBR uses this as its latency floor.
BDP = BtlBw × RTprop
The optimal in-flight data volume. BBR keeps congestion window near BDP — full link, empty queue.
Four-Phase Cycle
STARTUP, DRAIN, PROBE_BW, and PROBE_RTT cycle continuously to keep estimates fresh and adapt to path changes.
Linux kernel since 4.9 (2016). Deployed across Google's WAN, YouTube, and QUIC.

## Slide 4
What We Built: The Testbed
A reproducible, low-overhead environment using Linux network namespaces and traffic control — no VMs, no virtualization noise.
Topology
Two network namespaces on one CachyOS host (kernel 6.19), connected by a veth pair:
ns1 (server) — 10.0.0.1
ns2 (client) — 10.0.0.2
tc tbf + netem on the veth pair emulates the bottleneck
TSO/GSO/GRO disabled so packet-count queue limits reflect real packets.
Traffic Control Stack
tbf (root qdisc)
Enforces the rate limit on the bottleneck link.
netem (child qdisc)
Adds one-way delay and a packet-count queue limit. Applied symmetrically so RTT = 2 × one-way delay.
Traffic generated with iperf3 -C <bbr|cubic|reno>, JSON output at 100 ms intervals.

## Slide 5
EXPERIMENT 1
Throughput Sweep: 81 Configurations
We swept 3 CCs × 3 bandwidths × 3 delays × 3 buffer sizes — 81 runs at 30 seconds each — measuring how close each algorithm gets to the bottleneck cap.
Selected Results at 100 Mbps Bottleneck (% of link capacity)
One-Way Delay / Buffer
BBR
CUBIC
RENO
5 ms (10 ms RTT) — any buffer
95%
95%
95%
20 ms (40 ms RTT) — 100 pkt
95%
22%
11%
80 ms (160 ms RTT) — 100 pkt
95%
22%
11%
80 ms (160 ms RTT) — 1000 pkt
95%
95%
48%
Key Finding: At shallow buffers and high RTT, CUBIC and RENO collapse to 11–22% utilization. BBR holds near 95% across nearly every condition. The advantage grows with delay — exactly as the paper predicted.

## Slide 6
EXPERIMENT 2
Buffer Bloat: Same Throughput, 3× the Latency
A single 60-second flow per CC at 100 Mbps, 40 ms base RTT, and a 1000-packet buffer (~3× BDP). All three algorithms reached similar throughput — but latency tells a different story.
CC
Throughput
Mean RTT
RTT Inflation
Retransmits
BBR
93.4 Mbps
42.7 ms
1.07×
0
CUBIC
95.7 Mbps
120.3 ms
2.95×
92
RENO
95.6 Mbps
104.2 ms
2.56×
888
BBR's Advantage
BBR keeps latency at the propagation floor (~42 ms vs. 40 ms base). It never overfills the queue, resulting in zero retransmits in steady state.
Loss-Based Penalty
CUBIC and RENO inflate RTT by ~3× while achieving nearly identical throughput. RENO's 888 retransmits reflect aggressive queue overfilling and loss recovery cycles.

## Slide 7
EXPERIMENT 3
Fairness: Competing Flows on the Same Bottleneck
Two iperf3 flows competing on a 100 Mbps / 40 ms / 1000-pkt bottleneck. We measured steady-state share split and Jain's fairness index (1.0 = perfect fairness).
Pairing
Share Split
Jain's Index
Interpretation
BBR vs. CUBIC
0.58 / 0.42
0.973
Mild BBR advantage
BBR vs. BBR
0.53 / 0.47
0.995
Near-perfect fairness
CUBIC vs. CUBIC
0.64 / 0.36
0.932
Self-unfairness
BBR vs. BBR Baseline
Intra-protocol fairness converges almost perfectly (Jain = 0.995), confirming the testbed is well-calibrated.
BBR vs. CUBIC: Milder Than the Paper
BBR takes a modest 58/42 share — far less dramatic than the 2016 paper. Likely causes: a 3×-BDP buffer (vs. the paper's deeper multiples), single trial per pair, and lower jitter than Google's WAN traces.
BBRv2 Context
BBRv2 was created specifically to address BBR-vs-CUBIC fairness in deeper buffers, building on these findings.

## Slide 8
How Our Results Compare to the Paper
✅ Reproduced Cleanly
BBR matches link capacity regardless of buffer size
CUBIC and RENO under-utilize on shallow buffers + high RTT
BBR keeps RTT at the propagation floor; loss-based CCs inflate RTT 2.5–3×
BBR has zero retransmits in steady state
⚠️ Milder Than the Paper
BBR vs. CUBIC unfairness was modest (~58/42), not the dramatic split shown for deep buffers
Likely causes: 3×-BDP buffer, single trial per pair, lower jitter than Google's WAN traces
🔬 Scope Limitations
No lossy-link experiments (random loss via netem)
Multi-flow scaling limited to 2 flows
BBRv2 not evaluated

## Slide 9
Conclusions
1
Loss-Based CC Is a Latency Tax
BBR removes most of it by operating at the Kleinrock optimal point — full link, empty queue — without waiting for loss signals.
2
BBR's Win Is Context-Dependent
Largest on high-RTT shallow-buffer paths and deep-buffer paths where buffer bloat dominates. On short-RTT paths with small buffers, all CCs perform similarly.
3
Fairness Is the Tradeoff
BBR is mildly unfair to loss-based flows in deep buffers (~58/42 split). This motivated BBRv2, which tightens fairness while preserving latency benefits.
4
A Laptop Testbed Suffices
A controlled netns + tc setup reproduces the paper's qualitative claims — accessible, reproducible, and low-overhead.
Throughput isn't the whole story. Latency under load is what BBR fixes.